## Slide 1: Multi-Physics, Multi-Fidelity System Design Evaluation Simple Satellite Model
OpenMETA Design Study
Across
Geometry, Dynamics, Structural
Metamorph Software
Vanderbilt University
Ted Bapty (ted.bapty@metamorphsoftware.com / bapty@isis.vanderbillt.edu)

## Slide 2: What/Why/How
What?
  Tools for Design and Evaluation of Complex Systems
  Using Single Model to drive Multiple Analysis Tools
    E.g. CAD, FEA-Nastran,Abaqus, Dynamics-Modelica,Simulink, CFD-OpenFOAM, SPICE, SystemC, …
  Determine Best Design Choices, Architecture, Software. Predict System Performance/Cost Before You Build/Buy It.
Why?
  Subsystems & Components Interact in Many Complex Ways, Across Multiple Domains
  E.g. Component Choice Placement  Inertia, Thermal Interactions. InertiaControl Actuators & Algorithms. Actuators  Power Consumption & Thermal Source, …
  Maintaining Multiple System Models to Accomplish This Is Expensive, Error-Prone (Model Sync) and Time/Cost Prohibitive.
How?
  OpenMETA Design Tools Capture System Structure & Components
  OpenMETA Analysis Tools Auto-Compose Models for Other Common Tools (PTC Creo, NASTRAN, Dymola, Simulink
  Integrated MDAO Tools Execute Multi-Physics Analysis Campaigns, Leveraging Workstations and Cloud Computing
  Core Tools are Open Source – Metamorph Business Model is to Help Integrate Into Organizational Design Processes and Add Analysis Tool Support

## Slide 3: Who Can Use It, & How
Concept Evaluation
  Evaluate a Wide Range of Concept Designs to Help Determine:
    Requirement Feasibility And Cost Impact
    Concept Development and Rapid Evaluation for Proposed Solutions
  Evaluate Proposed Solutions
    Across Multiple Scenarios
    Validate Feasibility and Costing
Preliminary Design
  Evolve Model Detail and Fidelity
  Evaluate All Proposed Architectures to Choose Best Cost/Perf
  Determine Potential Side Effects And Requirements Satisfaction
Detailed Design
  Multiple Fidelity Analysis – Choose the Correct Tool for Accuracy and Compute Cost
Digital Thread – Single Model Auto Maps to All Analysis Tools
  Models are Executable In Many Ways
  Metamodel-Based Approach Allows Extension

## Slide 4: Single Model: (System Block Diagram)
Block Diagram
Solid Model
==

## Slide 5: Components: Aggregation of Domain Models
Solar flux in, power (IV) out Physical, inertial
Attitude set in, PID Contol
Physical, inertial
Mass, Physical BB
Dynamics
Geometry
Geometry
Dynamics
Examples….
OpenMETA
Component
Inside the
Component
Component
Domain
Models

## Slide 6: Component Dynamics Models
Low Fidelity, Lumped Parameter Models
Couple Rotational Dynamics, Electrical/Torque Relationships, Electrical Energy Management, and Control Against a Simple Scenario

## Slide 7: Controller/Inertial/Environment Model
Rotational
Dynamics
(1D Surrogate)
Controller
(Software)
Solar Irradiance
(1D Surrogate)
TBD: Separate into
Different components

## Slide 8: Battery/SuperCap Dynamics

## Slide 9: Gyroscope Power Consumption Model

## Slide 10: PV Array Electrical Model

## Slide 11: Design Analysis For Simple Spacecraft
Design Variables
  Solar Cell Size, Gyro/reaction wheel Size, Battery
  Geometry (Physical placement of components)
  Control Parameters (PID coeff)
  Mission Scenario (operations, rotations vs time)
Performance Parameters
  Power supply state (min/max V, average batt cap)
  Thermal behavior
  Time on station (within x of scenario)

## Slide 12: Geometry Analysis
Geometry Design Space
Metrics
2-Panel
3-Panel
4-Panel

## Slide 13: Dynamics Simulation Analysis
Metrics:
Min V = 4.5
Avg Angle Error: xxx
Max Thermal

## Slide 14: Structural Analysis Using FEA

## Slide 15: FEA Process
OpenMETA
System Model
Compose
Geometry
Initial
Meshing of
Geometry
MM / FeMAP
Mesh Update
Auto-Update Model
Study
Driver
Design Study
Auto-
Compose
Geometry
Mesh
Geometry
FEA Solution
Auto-Update Mesh
FEA Solution
Automated FeMAP
One-Time
Setup
Automated Execution
Across Discrete & Parametric Space

## Slide 16: Perform A Design Study
Evaluate Discrete Design Choices
  Solar Cells: 2-Panel, 3-Panel, 4-Panel
Evaluate Continuous Design Variables
  3D Placement of Payload Systems (Battery, Gyro, Electronics)
  Gyroscope/Reaction Wheel Sizing, Battery Sizing
  Material Thickness For Payload Mounts
  Controller Parameters
Design Metrics
  Power Bus Stability (Min/Max Voltage on Bus)
  Battery Charge Levels
  Angle Pointing Error
  Mount Component Material Stress Factor-of-Safety

## Slide 17: Standalone Dynamics Study
Visualize Results
Specify Study

## Slide 18: Standalone Geometry Study

## Slide 19: Initial Full System Study Workflow
CAD Model
Assembly
Dynamic
Sim
Mass, Moments
Thermal
Sim
Thermal
FEA
Power Demand &
Rotation Dynamics
Mesh
Thermal
Conductance /
Masses
Thermal Performance
Over Scenario Time
Scenario
Structural
FEA
Stress Factor of Safety

## Slide 20: Coupled Analysis
Inertia From Solid Model Drives
Dynamics Model (Rotational Inertia)

## Slide 21: Summary
Existing Tool Framework
  Has been used for Missile, Vehicle, Electronics Design.
  Missile Concept Study 3x Efficiency Gain
  Expandable – New Tools Can Be Added
Single Model Drives Multiple Tools
  Eliminate Labor/Model Inconsistency
  Rapid & Flexible Analysis, Employ Local or Cloud Compute
  Spans a Range of Commercial/Open Source Tools
Core Tools are Open Source
  But Leverage Commercial Best-In-Class Tools AND Open Source Tools
Also Supports Electronics Design Processes
  Plug Together Electronics Functional Blocks
  Generates Manufacturable Printed Circuit Boards

## Slide 22: Electronics Design with OpenMETA
1. Define Block Diagram: e.g. Processor, Antenna,
EKG, Blood Pressure
2. Place Blocks On Board
3. Tools Create PCB, Uses EagleCAD to Autoroute Intermodule Connections and Produce Manufacturable Data Package
Leverages a Library of Components
And Pre-Routed Subsystems (e.g. Sparkfun
Sensor Library, BLE uC Platforms, …)
Integrates: Spice, EagleCAD, SystemC, OpenEMS
R&D Topic: Integrate with Radiation-Effects
Analysis